## Slide 1
Introduction to NFV
Shamik Mishra

## Slide 2: Agenda
Introduction to NFV
  What is NFV
  Why Virtualize
ETSI NFV Framework
NFV Infrastructure Domain
  Compute Domain
  Hypervisor Domain
  Networking
NFV Management and Network Orchestration

## Slide 3: What is Network Function Virtualization (NFV)
Radio
Nodes
Router
Firewall
Load
Balancer
Distribution
Switch
Web
Servers
IMS
GW
MME
Today
Separate Network appliance for each Function
Dedicated or Proprietary Hardware for each function
Unused computing capability => Less agility
Separate Management Systems
Difficult to introduce new services rapidly => Less Agility
Higher Power Consumption, Real-estate => High Capex
Future
Network Functions hosted on Commodity Hardware through Virtualization
Scalable, Elastic and efficient usage of resources
Possibility of unified management and orchestration of services
Easy to introduce new functions => fast
Cost Effective
Promotes Open Innovation (is it so?)
Each Function Virtualized and Hosted on Commodity HW

## Slide 4: Why Virtualize?
Sharing
Isolation
Aggregation
Dynamics
Cost Reduction
Management
  When a resource is too big for a single user, it is best to divide it into multiple virtual pieces
  Each function can run on multiple VMs and each machine can be used by different users.
  The same applies to high-speed links and large-capacity disks
  Multiple users may not trust users, it is important to isolate users
  Provider should be able to share resources but easily isolate the data
  If the resource is too small, it is possible to construct a large virtual resource that behaves like a large resource and allocate resources to large number of appliances
  If computing capability is unused, it can be re-used for other network functions dynamically
  Rapidly scale-up / scale down services as required
  Optimize resources at real-time
  Virtual devices are easier to manage because they are software-based and expose a uniform interface through standard abstractions.
  Reduce CAPEX through less investment in energy, Real-estate and dedicated hardware

## Slide 5: NFV: Beyond Virtualization
Virtualization is an excellent way to cut expenses but it is equally challenging to manage and automate the virtualization environment

## Slide 6: NFV Framework
NFV Orchestrator (NFVO)
OSS / BSS
Virtual Infrastructure Manager (VIM)
VNF Manager (VNFM)
EMS
VNF
Computing Hardware
Storage Hardware
Network Hardware
Virtualization Layer
Virtual Computing
Virtual Storage
Virtual Network
NFVI
VI-Ha
EMS
VNF
EMS
VNF
Vn-Nf
VNFs
NFV MANAGEMENT AND NETWORK ORCHESTRATION (MANO)
Service, VNF and
Infrastructure Description
Os-Ma-nfvo
Ve-Vnfm
Nf-Vi
NFV Reference Points
Execution Reference Points
Or-Vi
Or-Vnfm
Vi-Vnfm

## Slide 7: NFV Infrastructure Domains
NFV Orchestrator (NFVO)
OSS / BSS
Virtual Infrastructure Manager (VIM)
VNF Manager (VNFM)
EMS
VNF
Computing Hardware
Storage Hardware
Network Hardware
Virtualization Layer
Virtual Computing
Virtual Storage
Virtual Network
NFVI
VI-Ha
EMS
VNF
EMS
VNF
Vn-Nf
VNFs
NFV MANAGEMENT AND NETWORK ORCHESTRATION (MANO)
Service, VNF and
Infrastructure Description
Os-Ma-nfvo
Se-Ma
Ve-Vnfm
Nf-Vi
Compute
Domain
Hypervisor Domain
Infrastructure Network
Domain

## Slide 8: NFVI
Compute Domain
Processor & Accelerator
Network Interfaces
Storage
Compute Architecture: x86 & ARM. Does not prevent other architectures
Accelerators: Security, Networking, Packet Processing
Network Capability Resident in Server (NIC connects to the processor via PCIe)
NIC may contain offload or acceleration functionality
Large Scale Storage, Non-Volatile storage (hard disks, solid state devices)
Possibility of Dis-aggregation
CPU Blades
NIC / Accelerators
Storage Blades
Separated CPU, Storage and NIC / Accelerators. Blades interconnected over Optical fibre.
Separating critical components from independently
VM
VM
VM
VM
VM
Compute Domain should support multiple virtual appliance. Simple words: able to virtualize
Ethernet
Fiber Channel
Infiniband
Physical Interfaces
Nf-Vi
External Interfaces
VIM

## Slide 9: NFVI
Hypervisor Domain
Virtual Switch
CPU Scheduler
Nf-Vi
External Interfaces
VIM
NIC
Core
Core
Core
Core
Memory Manager
Physical NIC Driver
HBA Driver
Guest OS
vNIC
vCPU
vMem
vHBA
vDisk
Virtual Machine
High Availability
Live Migration
Management Agent
Hypervisor Management
VNF
Compute Node
Storage
VNF
Vi-Ha
Virtual Machine Management APIs
Hypervisor Domain

## Slide 10: End to End Network Service
VNF Forwarding Graph
A
NF1
NF2
NF3
NF4
NF5
B
Forwarding
Graph-1
Forwarding
Graph-2
Virtualization Layer
End to End Network Service
Hardware Resources in
Physical Location
Physical Link
Logical Link
Virtualization

## Slide 11: Management and Network Orchestration
Concepts
NFV Orchestrator (NFVO)
Virtual Infrastructure Manager (VIM)
VNF Manager (VNFM)
NFV MANAGEMENT AND NETWORK ORCHESTRATION (MANO)
Os-Ma
Se-Ma
Ve-Vnfm
Nf-Vi
OSS / BSS
Service Description
VNFs
NFVI
Functional Blocks
Orchestrator:
– on-boarding of new Network Service (NS), VNF-Forwarding Graph and VNF Packages
– NS lifecycle management (including instantiation, scale-out/in, performance measurements, event correlation, termination)
– global resource management, validation and authorization of NFVI
resource requests
– policy management for NS instances
VNF Manager:
– lifecycle management of VNF instances
– overall coordination and adaptation role for configuration and event
reporting between NFVI and the E/NMS
Virtualized Infrastructure Manager (VIM):
– controlling and managing the NFVI compute, storage and network
resources, within one operator’s infrastructure sub-domain
– collection and forwarding of performance measurements and events

## Slide 12: VNF Forwarding Graph
Orchestration
NF1
NF2
NF3
A
B
Net1
Net2
A
NF1
NF2
NF3
B
Switch
Virtualized
NFV MANO
OSS
NFV Orchestration
Configuration
Service Instantiation
Automated
Automated
Automated
Automated
Automated
Automated

## Slide 13: Network Service Lifecycle Management
Simple Example
NFV Orchestrator (NFVO)
OSS / BSS
Network Service
VNF Packages
Network Service Instantiate
VNF Manager (VNFM)
Resource Allocation, Management, Optimization, Authorization
NFVI Resource Reservation
Virtual Infrastructure Manager (VIM)
Allocate / Update
VM Resources
Network Resources
NFVI
Network Service
Monitoring
VNFs
VNF Instantiation
EMS
EMS Instantiation
VNF Health Monitoring

## Slide 14: Management & Orchestration
Operations
1
2
3
4
Network Service Management
Virtualized Resource Management
VNF Management
NFVI Management
Network Service lifecycle management / Change Notification
Network Service performance management
Network Service fault management
Ex: Instantiate, Terminate, Query, Scale E2E Network Services
VNF Package management
VNF software image management
VNF lifecycle operation granting
VNF lifecycle management / Change Notification
VNF configuration
VNF performance management
VNF fault management
catalogue management
capacity management
Resource management
Performance management
Fault Management
Hypervisor management (Ex: create, suspend, delete, reboot, restore VMs)
Create, delete, list network, subnet, ports etc.

## Slide 15
Headquarters
303 Twin Dolphin Drive 6th Floor Redwood City, CA 94065 USA
Tel: +1 650 632 4310 Fax: +1 650 551 9901
APAC HQ
Plot 31, Electronic City Sector 18 Gurgaon, Haryana 122015 India
Tel: +91 124 4095888 Fax: +91 124 2455100
Europe HQ
Intec 4, Wade Road, Basingstoke, Hampshire RG24 8NE, United Kingdom
Tel: +44 1256 339500
Thank you.