## Slide 1: NETCONF

## Slide 2
NETCONF
Topics covered in this presentation :
Introduction and Overview
Protocol Layers
XML Considerations
RPC Model
Configuration Model
Protocol Operations
Protocol Capabilities

## Slide 3: INTRODUCTION
Protocol defined by IETF
Install, manipulate, delete configuration of network devices
XML-based encoding: protocol messages and configuration data

## Slide 4: Why NETCONF ?
Prior to NETCONF CLI Scripting used
Limitations:
- lack of transaction management
- no structured error management
- ever changing structure and syntax of commands that makes scripts fragile and costly to maintain
=> use NETCONF (reduced operational economy)

## Slide 5: NETCONF Protocol- Overview
uses RPC-based mechanism to carry our communication between client and server
- client (application running as a part of network manager)
- server (network device)
--------- <rpc> ------------>
<-------- <rpc-reply> ------
[secure connection-oriented session]
CLIENT
SERVER

## Slide 6
1 device – at least 1 session
Configuration attributes:
- Global: global to all sessions
- Session-specific: affect session in which changed
Information retrieved from running system:
- Configuration data: writeable data, transform system from initial state to desired operational state --> Configuration Datastore (complete set)
- State data: remaining (eg. user files, databases)

## Slide 7: NETCONF Protocol: Layers

## Slide 8
Secure Transport Layer
- communication between client, server
- Transport protocol satisfy:
    Connection-Oriented
    a) reliable and sequenced data delivery
    b) connection close- resources released
    Authentication, Integrity, Confidentiality
    authentication of both peers (eg. RADIUS – Remote Authentication Dial-In User Service)
    => authenticated identity of client = NETCONF username
    NETCONF implementation must support SSH transport protocol mapping

## Slide 9
2. Message Layer
- Provides transport-independent mechanism for encoding RPFs and notification.
- Messages: <rpc>, <rpc-reply>, notification
  (Notification message- sent from server to client indicating certain event has been recognized by the server)

## Slide 10
3. Operations Layer
- defines set of base protocol operations – invoked as RPC methods with XML-encoded parameters
  get
  get-config
  edit-config
  copy-config
  delete-config
  lock
  unlock
  close-session
  kill-session
- operation can be success (<ok>) or failure (<rpc-error>)

## Slide 11: XML Considerations
- All NETCONF messages – in well-formed XML, encoded in UTF-8.
If not - “malformed-message” error by the peer
- Namespace – for all elements:
urn:ietf:params:xml:ns:netconf:base:1.0

## Slide 12: RPC Model
- NETCONF uses RPC-based communication model
- Elements used by NETCONF:
  <rpc> element
  - to enclose netconf request sent from client to server
  - mandatory attribute: message-id
  - any other attribute returned unmodified by <rpc-reply>

## Slide 13
Example of <rpc>
Explanation
Method invoked: <my-own-method>
Parameters – Value pairs:
  <my-first-parameter> - 14
  <another-parameter> - fred

## Slide 14
  b) <rpc-reply> element
    to encloses response data from server to client
    mandatory attribute: message-id (same as <rpc>)
    - returns attributes in <rpc>, other than message-id, unmodified

## Slide 15: Example of <rpc-reply>

## Slide 16
Explanation
- <rpc>
Method invoked: <get>
Additional attribute: user-id
- <rpc-reply>
returns user-id attribute and requested content

## Slide 17
  b) <rpc-reply> element
    (i) <rpc-error> element
    - sent inside <rpc-reply> if error in processing of <rpc> request
    - if error conditions occur- at least 1 <rpc-error> mandatory
    - contains following information:
      error-type
      - defines concept layer on which error occurs
      - values:
      transport (layer = Secure Transport)
      rpc (layer = Message)
      protocol (layer = Operations)
      application (layer = Content)

## Slide 18
  2) error-tag
  - contains string identifying particular error condition
  eg. bad-attribute
  - Appendix A (page 76 onwards)
  3) error-severity
  - contains string identifying severity of error
  - values:
  error
  warning
  4) error-app-tag
  - a string identifying data-model specific/implementation specific error condition

## Slide 19
  5) error-path
  - contains the absolute XPath expression -- XML
  - identifies element path to the node associated with the
  error being reported in a particular <rpc-error> element
  6) error-message
  - string for human display to represent the error condition
  7) error-info
  - contains protocol/data-model specific error content
  - Appendix A (page 76 onwards) – standard Netconf errors

## Slide 20
Example of <rpc-error>
(Error reason: no <rpc> message-id attribute)
Eg. 1: single <rpc-error> element

## Slide 21
Eg. 2: multiple <rpc-error> elements

## Slide 22
  (ii) <ok> element
  - sent in <rpc-reply> if no error occurs while processing
  of <rpc> request and no data was returned from the
  operation

## Slide 23: Example of <ok> element

## Slide 24: Configuration Model
Configuration Datastore
- complete set of configuration data used to
transform state of network device: initial to
desired operational state
- doesn’t include state data
- 3 types: Running, Candidate, Startup

## Slide 25
  Running Configuration Datastore
- currently active on the network device
- <running> element
  Candidate Configuration Datastore
- configuration data which can be
manipulated without impacting device’s
current configuration
- <candidate> element

## Slide 26
  Startup Configuration Datastore
- loaded by the device when it boots
- <startup> element
Data Modelling
- done using YANG: Yet Another Next
Generation- to model configuration and state
data manipulated by Netconf)
- for reference:
  RFC 6020
  https://www.ietf.org/proceedings/86/slides/slides-86-i2rs-3.pdf

## Slide 27: Protocol Operations
NETCONF operation to manage device configuration ad retrieve device state information. The base protocol includes the following protocol operations:
lock
unlock
close-session
kill-session
get
get-config
edit-config
copy-config
delete-config

## Slide 28
Protocol Operations
<get-config> : Retrieve all or part of a specified configuration datastore
      Example: To retrieve the <running> configuration data:
          <rpc message-id="101"
          xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
          <get-config>
          <source>
          <running/>
          </source>
          </get-config>
          </rpc>
          <rpc-reply message-id="101"
          xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
          <data>
          <!– data -->
          </data>
          </rpc-reply>

## Slide 29
Protocol Operations
<edit-config> : Loads all or part of a specified configuration to the specified target configuration datastore. If the target configuration datastore does not exist, it will be created.
Attributes :
1. Operation : The attribute identifies the point in the configuration to perform the operation. If the "operation" attribute is not specified, the configuration is merged into the configuration datastore.
The "operation" attribute has one of the following values:
    merge
    replace
    create
    delete
    remove

## Slide 30
Protocol Operations
2. test-option: The <test-option> element MAY be specified only if the device advertises the :validate:1.1 capability
The “test-option" attribute has one of the following values:
Test-then-set
Set
Test-only
3. error-option: The <error-option> element has one of the following values:
Stop-on-error
Continue-on-error
Rollback-on-error

## Slide 31
Protocol Operations
Example: Set the MTU to 1500 on an interface named "Ethernet0/0" in the running configuration:
    <rpc message-id="101"
    xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
    <edit-config>
    <target>
    <running/>
    </target>
    <config>
    <top xmlns="http://example.com/schema/1.2/config">
    <interface>
    <name>Ethernet0/0</name>
    <mtu>1500</mtu>
    </interface>
    </top>
    </config>
    </edit-config>
    </rpc>

## Slide 32
Protocol Operations
<copy-config> : Create or replace an entire configuration datastore with the contents of another complete configuration datastore. If the target datastore exists, it is overwritten. Otherwise, a new one is created, if allowed.
Example:
    <rpc message-id="101"
    xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
    <copy-config>
    <target>
    <running/>
    </target>
    <source>
    <url>https://user:password@example.com/cfg/new.txt</url>
    </source>
    </copy-config>
    </rpc>

## Slide 33
Protocol Operations
<delete-config> : Delete a configuration datastore. The <running> configuration datastore cannot be deleted.
Example:
    <rpc message-id="101"
    xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
    <delete-config>
    <target>
    <startup/>
    </target>
    </delete-config>
    </rpc>
    <rpc-reply message-id="101"
    xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
    <ok/>
    </rpc-reply>

## Slide 34
Protocol Operations
<lock> : The <lock> operation allows the client to lock the entire configuration datastore system of a device. Such locks are intended to be short-lived and allow a client to make a change without fear of interaction with other NETCONF clients, non-NETCONF clients and human users.
Attempt to lock MUST failed if existing session or other entity holds a lock on any portion of the lock target.
The duration of the lock is defined as beginning when the lock is acquired and lasting until either the lock is released or the NETCONF session closes.
The <lock> operation takes a mandatory parameter, <target>. The <target> parameter names the configuration datastore that will be locked.

## Slide 35
Protocol Operations
A lock MUST NOT be granted if any of the following conditions is true:
A lock is already held by any NETCONF session or another entity.
The target configuration is <candidate>, it has already been modified, and these changes have not been committed or rolled back.
The target configuration is <running>, and another NETCONF session has an ongoing confirmed commit.
A lock will be released by the system if the session holding the lock is terminated for any reason.
An <rpc-error> element is included in the <rpc-reply> if the request cannot be completed for any reason. If the lock is already held, the <error-tag> element will be "lock-denied" and the <error-info> element will include the <session-id> of the lock owner.

## Slide 36
Protocol Operations
Example: The following example shows a successful acquisition of a
    lock.
    <rpc message-id="101"
    xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
    <lock>
    <target>
    <running/>
    </target>
    </lock>
    </rpc>
    <rpc-reply message-id="101"
    xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
    <ok/> <!-- lock succeeded -->
    </rpc-reply>

## Slide 37
Protocol Operations
<unlock> : The <unlock> operation is used to release a configuration lock, previously obtained with the <lock> operation.
An <unlock> operation will not succeed if
  The specified lock is not currently active.
  The session issuing the <unlock> operation is not the same session that obtained the lock.
Example:
    <rpc message-id="101"
    xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
    <unlock>
    <target>
    <running/>
    </target>
    </unlock>
    </rpc>
    <rpc-reply message-id="101"
    xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
    <ok/>
    </rpc-reply>

## Slide 38
Protocol Operations
<get> : Retrieve running configuration and device state information.
Example:
    <rpc message-id="101"
    xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
    <get>
    <filter type="subtree"></filter>
    </get>
    </rpc>
    <rpc-reply message-id="101"
    xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
    <data>
    <-data->
    </data>
    </rpc-reply>

## Slide 39
Protocol Operations
<close-session> : Request graceful termination of a NETCONF session. The server will release any locks and resources associated with the session
Example:
    <rpc message-id="101"
    xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
    <close-session/>
    </rpc>
    <rpc-reply message-id="101"
    xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
    <ok/>
    </rpc-reply>

## Slide 40
Protocol Operations
<kill-session> : Force the termination of a NETCONF session, it will abort any operations currently in process, release any locks and resources associated with the session, and close any associated connections.
Example:
    <rpc message-id="101"
    xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
    <kill-session>
    <session-id>4</session-id>
    </kill-session>
    </rpc>
    <rpc-reply message-id="101"
    xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
    <ok/>
    </rpc-reply>

## Slide 41
Capabilities
Each peer advertises its capabilities by sending them during an initial capabilities exchange. Each peer needs to understand only those capabilities that it might use and MUST ignore any capability received from the other peer that it does not require or does not understand.
Capabilities Exchange : messages sent by each peer during session establishment.<hello> element containing a list of that peer’s capabilities.
Each peer MUST send at least the base NETCONF capability, "urn:ietf:params:netconf:base:1.1".
A server sending the <hello> element MUST include a <session-id> element containing the session ID for this NETCONF session.
<hello xmlns="urn:ietf:params:xml:ns:netconf:base:1.0">
<capabilities>
<capability>
urn:ietf:params:netconf:base:1.1
</capability>
http://example.net/router/2.3/myfeature
</capability>
</capabilities>
<session-id>4</session-id>
</hello>

## Slide 42
Capabilities
Each peer sends its <hello> element simultaneously as soon as the connection is open. A peer MUST NOT wait to receive the capability set from the other side before sending its own set. Some types of capabilities are :
Writable-Running Capability :The :writable-running capability indicates that the device supports direct writes to the <running> configuration datastore.
Candidate Configuration Capability : The candidate configuration capability, :candidate, indicates that the device supports a candidate configuration datastore, which is used to hold configuration data that can be manipulated without impacting the device’s current configuration.
Confirmed Commit Capability: The :confirmed-commit:1.1 capability indicates that the server will support the <cancel-commit> operation and the <confirmed>, <confirm-timeout>, <persist>, and <persist-id> parameters for the <commit> operation.

## Slide 43
Rollback-on-Error Capability :This capability indicates that the server will support the "rollback-on-error" value in the <error-option> parameter to the <edit-config> operation.
Validate Capability :Validation consists of checking a complete configuration for syntactical and semantic errors before applying the configuration to the device.
Distinct Startup Capability :The device supports separate running and startup configuration datastores. The startup configuration is loaded by the device when it boots.
URL Capability : The NETCONF peer has the ability to accept the <url> element in <source> and <target> parameters. The capability is further identified by URL arguments indicating the URL schemes supported.
XPath Capability : The XPath capability indicates that the NETCONF peer supports the use of XPath expressions in the <filter> element.
Capabilities

## Slide 44: Thank you !